## Slide 1
ECE-321
15-05-2024
Mariam Mohamed Gadallah 120210299
Eyad Mohamed Ossman 120210309
Mohamed Moataz Sallam 120210343
Youssef Mohamed Hatem 120210359
Companion Robot for the Visually Impaired
Supervised by:
Prof. Adel Bedair Prof. Moataz Abdelwahab

## Slide 2
Introduction
What is the aim of the project?
ECE-319
ECE-319
ECE-321
The robot aim is to guide a visually impaired person through a room, the robot scans the room then guide the person through voice instructions.
It uses 4 ultrasonic sensors to scan the room and the rotary encoders to get the map readings.
Figure 1: Robot scanning a room

## Slide 3
Project Components
ECE-319
ECE-321
Arduino Uno
Ultrasonic Sensors [HC-SR04] x4
L298N motor Driver
Rotary Angle Encoder x2
DC Motors x2
MP3 Player
Speaker
Battery
Figure 2: Connection schematic

## Slide 4
ECE-319
ECE-321

## Slide 5
Methodology
What are the rotary encoders used for ?
ECE-319
ECE-319
ECE-321
Figure 3: Incremental rotary encoder
Rotary encoders generates electrical pulses as the shaft turns. These pulses are interpreted by a controller to determine direction and distance of rotation.
They are used to take the reading from the wheel. When it rotates 10 times it means it has navigated a full cell which helps in creating the room map.
Figure 4: Rotary encoder working principle

## Slide 6
Methodology
How does the robot scan a room?
ECE-319
ECE-319
ECE-321
Figure 5: Actual example of a map
0 1 2 3 4 5 6 7 8 9
It moves in odd columns while detecting the current cell as well as the left, right, and front cells via the four ultrasonic sensors.
The robot iterates on most cells twice to achieve a minimal error percentage.
| Not yet detected
O Free
X Obstacle

## Slide 7
Methodology
Using PID Controller to make up for motor synchronization deficiency
ECE-319
ECE-319
ECE-321
Figure 6: Rotary encoder
Proportional (P): Adjusts output proportionally to current error.
Integral (I): Accumulates past errors to eliminate steady-state error.
Derivative (D): Predicts future errors by considering error rate of change to control system overshoot.
Figure 8: Non-zero steady state error
Figure 7: graphical representation of overshoots

## Slide 8
Real-life
Demo
ECE-319
ECE-319
ECE-321
Figure 4: Rotry encoder

## Slide 9
Future Plans
ECE-319
ECE-319
ECE-321
Figure 9: Robot Operating System
Fine-tune the controller parameters.
Use Robot operating System(ROS) for better control over multiple units.
Implement Dijkstra’s Algorithm to find the shortest route to a certain destination.
Apply Kalman filter on rotary encoder readings.

## Slide 10
References
1 | Banzi, M. (2011). Getting Started with Arduino. Maker Media, Inc.
2 | Monk, S. (2012). Programming Arduino: Getting Started with Sketches. McGraw-Hill Education
3 | Margolis, M. (2014). Arduino Cookbook. O'Reilly Media.
4 | McRoberts, M. (2011). Beginning Arduino. Apress.
5 | Lang, M. (2013). Arduino Project Handbook: 25 Practical Projects to Get You Started. No Starch Press.
6 | Upton, E., & Halfacree, G. (2016). Raspberry Pi user guide. John Wiley & Sons.

## Slide 11
Questions?